## Slide 1: Network Fundamentals for Cloud
Nishit Narang
WILPD-CSIS

## Slide 2
CC ZG503: Network Fundamentals for Cloud
Lecture No. 1

## Slide 3
Introductions

## Slide 4
Head and Associate Professor, Computer Science and Information Systems, Off Campus BITS Pilani (joined Dec 2020)
Academic Background:
B.Tech and PhD from IIT Delhi in Computer Science and Engineering
Expertise:
Computer & Communication Networks and Information Security
Faculty Introduction – Dr Nishit Narang
Past Experience:
Before BITS Pilani, worked for 23 years in the IT industry
Projects in terrestrial, satellite, and mobile communication networks, Industrial and Consumer IoT solutions involving industrial automation, smart city solutions, and consumer wearables
Over the years and across projects, focused extensively on Information Security and Cybersecurity.
Books Authored:
Co-author of four books in the communications domain, which are published by McGraw Hill and sold internationally

## Slide 5
Course Introduction: Objectives
No | Description
CO1 | Understanding design and architectural choices for a data center network.
CO2 | Understand enabling technologies, protocols, tools and services used for implementation of cloud networks.
CO3 | Understanding cloud network performance and security challenges and methods to address them.

## Slide 6: Course Structure Overview
Network Fundamentals
Enabling Technology Overview
Data Center Networks
(Physical Network)
Virtual Cloud Networks
Network Topologies
TCP/IP Reference Model
Addressing Concepts
Routing and Switching Functions
VPNs and VLANs
Reliability in Data Transfer
Congestion Control, Flow Control and Traffic Engineering
Network Performance and Security

## Slide 7: Course Structure Overview
Network Fundamentals
Enabling Technology Overview
Data Center Networks
(Physical Network)
Virtual Cloud Networks
Software Defined Networking
Network Function Virtualization
Network Performance and Security

## Slide 8: Course Structure Overview
Network Fundamentals
Enabling Technology Overview
Data Center Networks
(Physical Network)
Virtual Cloud Networks
DCN Traffic Patterns and Challenges
DCN Architecture and Network Topologies
Routing Protocols for DCNs
Multi-DC Networks
SDN in the Data Center
Network Performance and Security

## Slide 9: Course Structure Overview
Network Fundamentals
Enabling Technology Overview
Data Center Networks
(Physical Network)
Virtual Cloud Networks
Virtual Private Cloud
SR-IOV, vSwitch, OVS
Cloud DNS, Cloud NAT, Cloud VPNs
API Gateways, ALBs, CDN
Container Networking
Network Performance and Security

## Slide 10: Course Structure Overview
Network Fundamentals
Enabling Technology Overview
Data Center Networks
(Physical Network)
Virtual Cloud Networks
Cloud Network Security
Hypervisor Risks
Network Segmentation
Firewalls, Access Security Brokers, IPS
Traffic Monitoring & Visualization
Network Performance & Optimization
Network Performance and Security

## Slide 11
Text & Reference Books
Text Book(s) | 
T1 | Kurose James F and Keith W. Ross: Computer Networking: A Top-Down Approach, Pearson India, 6th Edition, 2013
T2 | Lei Zhang, Le Chen. Cloud Data Center Network Architectures and Technologies, CRC Press 2021
T3 | Dinesh G. Dutt. Cloud Native Data Center Networking: Architecture, Protocols and Tools, O’Reilly 2020
R1 | Paul Goransson, Chuck Black. Software Defined Networks: A Comprehensive Approach, MK (Elsevier) 2014
R2 | Ken Gray, Thomas D. Nadeau. Network Function Virtualization, MK (Elsevier) 2016
R3 | Ronald L. Krutz, Russell Dean Vines. Cloud Security: A Comprehensive Guide to Secure Cloud Computing, John Wiley & Sons, 2010

## Slide 12
Supporting Material
Other Reading Material | 
O1 | Jupiter Rising: A Decade of Clos Topologies and Centralized Control in Google’s Datacenter Network by Arjun Singh and Others
O2 | A Scalable, Commodity Data Center Network Architecture by Mohammad Al-Fares, Alexander Loukissas and Amin Vahdat
O3 | B4: Experience with a Globally-Deployed Software Defined WAN by Sushant Jain and Others
O4 | Cloud Service Provider (AWS, Azure, GCP) Public Domain Technical Documentation

## Slide 13
Proposed Evaluation Scheme
No | Name | Type | Duration | Weight
EC-1 | Quiz-I | Online | - | 5%
EC-1 | Quiz-II | Online | - | 5%
EC-1 | Assignment-I | Online | - | 10%
EC-1 | Assignment-II | Online | - | 10%
EC-2 | Mid-Semester Test | Closed Book | 2 hours | 30%
EC-3 | Comprehensive Exam | Open Book | 3 hours | 40%

## Slide 14
Fundamentals of Networking: Part 1
Slides Source: Computer Networking: A Top-Down Approach, 8th edition, Jim Kurose, Keith Ross, Pearson, 2020
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 15: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 16: The Internet: a “nuts and bolts” view
Internet: “network of networks”
  Interconnected ISPs
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Ethernet
HTTP
Skype
IP
WiFi
4G
TCP
Streaming
video
Internet standards
  RFC: Request for Comments
  IETF: Internet Engineering Task Force

## Slide 17: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events

## Slide 18: What’s a protocol?
A human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 19: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers

## Slide 20: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links

## Slide 21: A closer look at Internet structure
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links
Network core:
  interconnected routers
  network of networks
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 22: Access networks and physical media
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks (WiFi, 4G/5G)

## Slide 23: Access networks: enterprise networks
companies, universities, etc.
  mix of wired, wireless link technologies, connecting a mix of switches and routers (we’ll cover differences shortly)
    Ethernet: wired access at 100Mbps, 1Gbps, 10Gbps
    WiFi: wireless access points at 11, 54, 450 Mbps
Ethernet
switch
institutional mail,
web servers
institutional router
Enterprise link to
ISP (Internet)

## Slide 24: Access networks: data center networks
high-bandwidth links (10s to 100s Gbps) connect hundreds to thousands of servers together, and to Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Courtesy: Massachusetts Green High Performance Computing Center (mghpcc.org)

## Slide 25: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=