## Slide 1: Network Fundamentals for Cloud
Nishit Narang
WILPD-CSIS

## Slide 2
CC ZG503: Network Fundamentals for Cloud
Lecture No. 7: SDN and NFV

## Slide 3
Software Defined Networking (SDN)
Some Slides Taken and Adapted from:
Computer Networking: A Top-Down Approach, 8th edition, Jim Kurose, Keith Ross, Pearson, 2020
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 4: Network layer: data plane, control plane
Data plane:
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
1
2
3
0111
values in arriving
packet header
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers

## Slide 5: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 6: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 7
Lets Look into…,
Traditional Switch Architecture
Evolution of Switches, Control Planes and needs of Modern Data Centers

## Slide 8
Evolution of Switches and Control Planes
Traditional Switch Architecture
Data Plane
  Vast majority of packets only touch data plan
  Contains
    Reception & Transmission Ports
    Forwarding Table
What does the Data Plane do?
  Packet buffering
  Packet scheduling
  Header modification and forwarding
What happens if the packet information is not in the forwarding table?
  Data Plane communicates vertically to Control Plane

## Slide 9
Evolution of Switches and Control Planes
Traditional Switch Architecture
Control Plane
  Principal role - Keep forwarding table up-to-date
  Control plane of the switch is bombarded with a constant barrage of control protocol traffic
  Process control protocols - Control protocols collectively manage the topology of the network.
Management Plane
  Network administrators configure and monitor the switch through this plane
  Interfaces vertically to collect or update information in other planes
  Typically a NMS (network management system) communicates to the plane in the switch.

## Slide 10
Evolution of Switches and Control Planes
Developers  implemented distributed environment with intelligence in each device
Coordination between devices  Collective decisions
Goals
  Simplicity
  Ease of use
  Automatic Recovery
Distributed Intelligence in L2 and L3
    Spanning Tree Protocol (STP) – IEEE 802.1D
      Enforces a hierarchy on the network, Convergence latency
    Rapid Spanning Tree Protocol (RSTP) – IEEE 802.1D-2004
      Improves latency, but not deployed
    Shortest Path Bridging (SPB)
    RIP, BGP, OSPF, and IS-IS
        Layer 3 requires the cooperation between devices, Knowledge of which routers are attaching to which subnets in a network.

## Slide 11
This Programmable hardware gives life to the “concept of SDN”
Software-Based Routing and Bridging
  Ethernet interface speed increased through the 90’s.
  Hardware solutions leveraged to help routers and bridges keep up with increasing speed
  Eventually software could not keep up with header inspection and routing table lookups
Generically Programmable Forwarding Rules
  Early routers – limited packet header field mods.
  Switch features grew over time
    Multi-cast, VLANs, MPLS, etc.
    Pushing programmable rules to the hardware allows complex manipulation while maintaining line rates
Evolution of Switches and Control Planes

## Slide 12
WWW leads to
  Large data centers with huge numbers of servers and even greater VMs
Protocols designed to provide robustness over geographic area not appropriate for the huge amount of traffic in the DC
  Routers spend 30% of CPU cycles in rediscovery and recalculating routes
  East / West traffic doesn’t benefit from overhead of protocols.
  SDN was designed to handle the network of the modern data center  fundamental shift from traditional Internet switching
Modern Data Center
Modern Data Center

## Slide 13
SDN Architecture
SDN general
Architecture

## Slide 14
SDN Architecture
A three-layer
distributed
SDN Architecture

## Slide 16: Generalized forwarding: match plus action
1
2
0111
3
values in arriving
packet header
Review: each router contains a forwarding table
“match plus action” abstraction: match bits in arriving packet, take action
  generalized forwarding:
    many header fields can determine action
    many action possible: drop/copy/modify/log packet
forwarding table
(aka: flow table)
(aka: flow table)
  destination-based forwarding: forward based on dest. IP address

## Slide 17: Flow table abstraction
flow: defined by header field values (in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Router’s flow table define router’s match+action rules
Flow table
match
action

## Slide 18: Flow table abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)

## Slide 19: OpenFlow: flow table entries
Match
Action
Stats
Forward packet to port(s)
Drop packet
Modify fields in header(s)
Encapsulate and forward to controller
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer

## Slide 20: OpenFlow: examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
Block (do not forward) all datagrams destined to TCP port 22 (ssh port #)
Block (do not forward) all datagrams sent by host 128.119.1.1
Destination-based forwarding:
*
*
*
*
*
*
51.6.0.8
*
*
*
port6
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
*
*
Firewall:
drop
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
drop
*
128.119.1.1

## Slide 21: OpenFlow: examples
Layer 2 destination-based forwarding:
layer 2 frames with destination MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
*
*
*
*
*
*
*
*
*
port3
22:A7:23:
11:E1:02
*
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS

## Slide 22: OpenFlow abstraction
match+action: abstraction unifies different kinds of devices
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port

## Slide 23: OpenFlow example
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 24: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 25: Generalized forwarding: summary
“match plus action” abstraction: match bits in arriving packet header(s) in any layers, take action
  matching over many fields (link-, network-, transport-layer)
  local actions: drop, forward, modify, or send matched packet to controller
  “program” network-wide behaviors
simple form of “network programmability”
  programmable, per-packet “processing”
  historical roots: active networking
  today: more generalized programming

## Slide 26
Network Function Virtualization (NFV)
Some Slides Taken and Adapted from:
Computer Networking: A Top-Down Approach, 8th edition, Jim Kurose, Keith Ross, Pearson, 2020
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 27: Virtualization Concept

## Slide 28
Network Virtualization
What is network virtualization ?
  In computing, Network Virtualization is the process of combining hardware and software network resources and network functionality into a single, software-based administrative entity, a virtual network.
Two categories :
  External network virtualization
    Combining many networks, or parts of networks, into a virtual unit.
  Internal network virtualization
    Providing network-like functionality to the software containers on a single system.

## Slide 29
Network Virtualization
What is network virtualization ?

## Slide 30
Network Virtualization
Desirable properties of network virtualization :
  Scalability
    Easy to extend resources in need
    Administrator can dynamically create or delete virtual network connection
  Resilience
    Recover from the failures
    Virtual network will automatically redirect packets by redundant links
  Security
    Increased path isolation and user segmentation
    Virtual network should work with firewall software
  Availability
    Access network resource anytime

## Slide 31
Network Virtualization
External network virtualization in different layers :
  Layer 1
    Seldomly implemented in physical data transmission layer.
  Layer 2
    Use some tags in MAC address packet to provide virtualization.
    Example, VLAN.
  Layer 3
    Use some tunnel techniques to form a virtual network.
    Example, VPN.
  Layer 4 or higher
    Build up some overlay network for some application.
    Example, P2P.

## Slide 32
Network Virtualization
Internal network virtualization in different layers :
  Layer 1
    Hypervisor usually do not need to emulate the physical layer.
  Layer 2
    Implement virtual L2 network devices, such as switch, in hypervisor.
  Layer 3
    Implement virtual L3 network devices, such as router, in hypervisor.
  Layer 4 or higher
    Layer 4 or higher layers virtualization is usually implemented in guest OS.

## Slide 33: Virtual LANs (VLANs): motivation
Computer
Science
EE
Q: what happens as LAN sizes scale, users change point of attachment?
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy issues

## Slide 34: Virtual LANs (VLANs): motivation
administrative issues:
CS user moves office to EE - physically attached to EE switch, but wants to remain logically attached to CS switch
Computer
Science
EE
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy, efficiency issues
Q: what happens as LAN sizes scale, users change point of attachment?

## Slide 35: Port-based VLANs
1
8
2
7
9
16
10
15
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local Area Network (VLAN)
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
… operates as multiple virtual switches
1
8
2
7
EE (VLAN ports 1-8)
…
9
16
10
15
…
CS (VLAN ports 9-15)

## Slide 36: Port-based VLANs
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 37: VLANS spanning multiple switches
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
5
8
2
7
…
16
1
6
3
4
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports

## Slide 38
Internal Network Virtualization
Properties of virtual switch
  A virtual switch works much like a physical Ethernet switch.
  It detects which VMs are logically connected to each of its virtual ports and uses that information to forward traffic to the correct virtual machines.
Typical virtual network configuration
  Communication network
    Connect VMs on different hosts
  Storage network
    Connect VMs to remote storage system
  Management network
    Individual links for system administration

## Slide 39
Internal Network Virtualization
Network virtualization example: VMware